## Slide 1: CNN-LSTM Based Network Traffic Forecasting
B.TECH FINAL-YEAR PROJECT · PROJECT REVIEW
Proactive Network Congestion Avoidance
Presented by
[Your Name]
Registration No.
[Registration Number]
Course
[Course / Project Title]
ATLA-M5
ATLA
CHIN
DNVR
HSTN
IPLS
KSCY
LOSA
NYCM
SNVA
STTL
WASH
Abilene (Internet2) backbone, 2004: 12 routers drawn at their real locations.
Thick: 9.92 Gbit/s links; amber: the 2.48 Gbit/s ATLA–IPLS link.
Notes: Introduce the project: forecasting traffic between router pairs on a real backbone network (Abilene), so that future link loads can be estimated and congestion flagged early. The map is drawn from the dataset's own topology file. Replace the bracketed name, registration number and course before presenting.

## Slide 2: Why Predict Traffic Before Congestion?
Traffic never stays still
Each router pair's traffic rises and falls through the day (peak about 1.5× the low point).
Congestion is handled after the fact
Reactive control acts only once a link is overloaded, so users already see delay and loss.
Minutes of warning are valuable
Forecasting traffic a few minutes ahead gives early information about future link load.
Project aim Forecast the traffic of all 144 origin-destination flows 5 minutes ahead, then use the forecasts for proactive congestion warnings.
Historical Traffic
Traffic Prediction
Future Link Load
Early Congestion Warning
Proactive Action
PHASES 1–5: FORECASTING
in progress
PHASE 6: APPLICATION
planned
Notes: Reactive congestion handling waits until a link is overloaded. If each origin-destination flow can be forecast a few minutes ahead, those forecasts can be turned into future link loads and early warnings. The teal steps are what the project has built so far; the dashed amber steps are the planned application phase.

## Slide 3: Abilene Dataset & Data Pipeline
12
routers
144
origin-destination flows
5 min
between readings
24
weekly files
2,016
readings per week
realOD = the measured traffic (first of 5 values per flow; the other 4 are model estimates). Unit: 100 bytes per 5 minutes.
Raw Abilene data
Cleaning
Remove invalid / outage periods
Segment continuous periods
log1p transform
Per-flow min–max scaling
Sliding 1-hour windows
Train / Val / Test
Chronological split: never shuffled, so the model is always tested on the future
Train 60% · 24,448 windows
Validation 20% · 8,149
Test 20% · 8,150
time: March → September 2004
Notes: Abilene: 12 routers give 144 origin-destination flows, one reading every 5 minutes, 24 weekly files of 2,016 readings. Each flow has 5 values; the first, realOD, is the real measurement. The pipeline cleans the data, cuts it into continuous segments, applies log1p and per-flow min-max scaling (fitted on training data only), builds 1-hour windows and splits them in time order 60/20/20.

## Slide 4: Data Cleaning: What Was Found and Fixed
Problems found in the raw data
Discontinuous weeks
README dates have gaps (e.g. 8 March → 2 April)
Duplicated days
4 weeks start with an exact copy of the previous day
Long flow outage
All traffic into ATLA-M5 reads zero for 22 days
Router outages
KSCY (1.5 h) and LOSA (~2 h) report nothing
Impossible value
~142 Tbit/s on a network whose fastest link is 9.92 Gbit/s
Normal zeros in small flows
Kept: real readings under 1-in-100 packet sampling
Rule | Detects | Steps removed
R1 Duplicate | Exact copy of the previous week's last day | 1,152
R2 Flow outage | Active flow at zero for ≥ 1 day | 6,336
R3 Router outage | All traffic in/out of a router zero ≥ 1 h | 40
R4 Impossible value | Above the 9.92 Gbit/s link capacity | 1
84.4%
of all time steps kept
(40,855 of 48,384)
Why keep normal zeros? With only 1 packet in 100 sampled, small flows really record nothing in some 5-minute slots. Removing them would delete real data.
Clean data
9 continuous segments
1-hour windows (12 × 144)
Prediction target (next 5 min)
Notes: Before modelling, the raw files needed cleaning. Four automatic rules remove duplicated days, long flow outages, router outages and one impossible value; everything else is kept, including the ordinary zeros in small flows. Removed steps are dropped, not filled in, so the model is never trained or scored on invented numbers. 84.4% of time steps remain, in 9 continuous segments; windows never cross a gap.

## Slide 5: Input/Output Design & CNN-LSTM Architecture
Input
12 readings × 144 flows = the last 1 hour of traffic (144 flows shown abbreviated)
Output
144 predicted values = each flow's traffic 5 minutes ahead
Input (12 × 144)
Conv1D · 64 filters · kernel 3 · causal
27,712
Conv1D · 64 filters · kernel 3 · causal
12,352
MaxPooling1D (2)
0
LSTM · 100 units
66,000
LSTM · 50 units
30,200
Dropout · 0.2
0
Dense · 144 outputs
7,344
parameters
CNN
Detects short-term patterns across neighbouring 5-minute readings. Causal: never sees a later reading.
LSTM
Learns how those patterns evolve over time.
143,608 parameters in the planned model (checked in code)
PLANNED MODEL · TRAINED IN PHASE 4
Notes: Input: 12 consecutive readings of all 144 flows, one hour. Output: 144 values, each flow 5 minutes ahead. The planned CNN-LSTM: two causal 1-D convolutions pick up short-term patterns, max pooling halves the sequence, two LSTM layers model how the patterns evolve, dropout limits memorising, and a dense layer outputs the 144 forecasts. Causal padding means no step can see a later reading, so there is no future leakage. 143,608 parameters, small enough for a laptop CPU. This hybrid has not been trained yet; that is Phase 4.

## Slide 6: Experimental Methodology & Baselines
1
Persistence
next value = current value
DONE
2
ARIMA
statistical baseline, 5 busiest flows
DONE
3
LSTM-only
planned model without the CNN
DONE
4
CNN-only
planned model without the LSTM
DONE
5
CNN-LSTM
the planned hybrid
PHASE 4
6
Residual / tuned models
residual LSTM & CNN done; tuning planned
PARTLY DONE
THE BAR TO BEAT
Next traffic value = current traffic value
Persistence needs no training, yet at 5-minute steps it is hard to beat. Every learned model must beat it, or improve on it meaningfully.
MAE
Average absolute error, in Mbit/s
RMSE
Like MAE, but large misses count more
MAPE
Error as a percentage of the true value
MAPE coverage
Share of values MAPE uses (true value ≥ 10% of average)
Validation data picks settings and stops training; test data is used once, at the end. Errors are measured in Mbit/s after undoing the scaling.
Notes: Models are compared in a fixed order, from the simplest baseline up to the hybrid. Persistence, ARIMA, LSTM-only, CNN-only and the residual LSTM and CNN are done; the CNN-LSTM and tuning are Phase 4. Metrics: MAE and RMSE in Mbit/s, MAPE with its coverage, because MAPE explodes on near-zero flows and is only computed where the true value is at least 10% of the average.

## Slide 7: Results So Far: Baselines & Single Models
Chart: Test MAE, all 144 flows (Mbit/s, lower is better)
| Persistence | LSTM-only | CNN-only | LSTM-only, residual | CNN-only, residual
Test MAE (Mbit/s) | 3.212 | 9.076 | 10.821 | 3.226 | 3.222
2.8×
worse than persistence
LSTM-only, as planned (9.076)
3.4×
worse than persistence
CNN-only, as planned (10.821)
≈ 0.3%
from persistence
Residual LSTM 3.226 · residual CNN 3.222
5 busiest flows only (test MAE, Mbit/s)
Persistence | 21.28
ARIMA | 21.87
LSTM-only, residual (best) | 21.25
CNN-only, residual | 21.31
Not yet done: the CNN-LSTM hybrid has not been trained (Phase 4), so no CNN-LSTM result is claimed here.
Notes: All numbers are test-split MAE in Mbit/s. Over all 144 flows, persistence scores 3.212. The LSTM-only and CNN-only models as planned are 2.8x and 3.4x worse. The residual versions bring the error down to 3.226 and 3.222, level with persistence. ARIMA was only run on the 5 busiest flows, so it is compared there: persistence 21.28, ARIMA 21.87, residual LSTM 21.25, the only model to edge past both. The CNN-LSTM has not been trained yet.

## Slide 8: Key Findings & Analysis
Residual learning
Current value
(persistence)
Learned correction
(network output, starts at 0)
Future prediction
LSTM-only test MAE: 9.076 → 3.226 Mbit/s
(as planned → residual)
1
Persistence is a very strong baseline at 5-minute steps.
2
Predicting the traffic level from scratch performed poorly (2.8–3.4× worse).
3
Residual learning cut the error by about two thirds.
4
Residual models learn a small correction to the latest value.
5
Residual LSTM edges past persistence on the 5 busiest flows (21.25 vs 21.28).
6
Sudden bursts are hard: the planned models stay near typical levels.
7
One bursty flow, LOSA→CHIN (bursts to ~6.5 Gbit/s), drives much of the error.
8
Predicting a correction suits this task better than predicting the full level.
Notes: Main lesson so far: at 5-minute steps the best predictor of the next value is the current one. Models that predict the level from scratch drift towards typical values and lose badly. A residual model starts from the current value and only learns a correction; it cut the error by about two thirds and is now level with persistence, slightly ahead on the 5 busiest flows. The LOSA to CHIN flow, which bursts to about 6.5 Gbit/s, shows why bursts are hard. Open question for Phase 4: the residual LSTM is 28% better than persistence in its training loss but only level in Mbit/s; a loss closer to MAE will be tested.

## Slide 9: Next: Proactive Congestion Avoidance
FUTURE WORK · NOT YET COMPLETED
CNN-LSTM prediction
Predicted OD traffic (144 flows)
Routing matrix
Predicted link loads
Compare with link capacity
Congestion risk
Early warning / proactive action
Routing matrix
54 × 144
links × flows
30 backbone links (28 at 9.92 Gbit/s, 2 at 2.48 Gbit/s)
24 entry/exit points at the routers
Each flow follows one defined path
Link loads = matrix × traffic
Already parsed and checked in Phase 1
Phase 4
Train the CNN-LSTM; tune one setting at a time; test a loss closer to MAE
Phase 5
Longer horizons: 6 and 12 steps (30 and 60 min); ablation/depth experiments
Phase 6
Future link loads, congestion warnings, GÉANT generalisation test
Phase 7
Detailed error analysis on traffic peaks; final report
Notes: Everything on this slide is planned, not done. Forecasts of the 144 flows will be multiplied by the routing matrix to get predicted loads on each link, compared with link capacity, and turned into early warnings. The routing matrix itself is already parsed and checked: 54 links by 144 flows, each flow on one path. Remaining phases: train and tune the CNN-LSTM, longer horizons and ablations, the congestion application and the GEANT dataset, then error analysis and the final report.

## Slide 10: Conclusion
Network traffic as 144 origin-destination flows, measured every 5 minutes
History turned into 1-hour input windows (12 × 144) for 5-minute-ahead forecasts
CNN layers: designed to capture short-term traffic patterns
LSTM layers: designed to capture how those patterns evolve over time
Residual learning cut neural-model error by about two thirds vs direct prediction
Next: complete the CNN-LSTM and connect forecasts to proactive congestion detection
Predict the traffic before congestion happens.
Thank You
Questions?
Notes: Summary: the network is modelled as 144 flows; one hour of history predicts the next 5 minutes; the CNN and LSTM layers have complementary roles; the clearest result so far is that residual learning is essential. The next step is the CNN-LSTM itself and then the link-load and congestion-warning application.